## Slide 1
RF Interference
Mitigation Strategies using Wideband Signal Recording

## Slide 2
Agenda
Interference in Many Forms
Use Cases and Need for Interference Testing
Challenges with Traditional Approaches
Alternative Approaches to Long-Duration Interference Testing
Case Studies
Tools for Interference Testing
Mitigation Strategies
Summary
X-COM Systems LLC™

## Slide 3
Radio
Conversations
Telemetry
Links
Flight
Range Ops
SIGINT
Spectrum
Monitoring
Required: Seconds, Minutes or Days of Seamless RF Signal Capture
The Need for Interference Testing
System
Interoperability

## Slide 4
Difficult to detect or predict signals of interest
  Unauthorized emissions
  Unpredictable interactions (Interoperability) in complex RF environments
Streamed signals are information
  Undeniable proof of what happened
  Use data to find other data
  Modify and replay recordings to stress and margin test receivers
  Characterize precise behavior in multiple domains
  Terabyte memories provide capture times from minutes to days
Need for RF Record & Playback
Lockheed Martin F-35 Joint Strike Fighter
Next Generation Smart Transportation Testing
Image Courtesy of University of Waterloo, Ont. World-class facility that could lead to the creation of new wireless technologies for use in smartphones, cars, healthcare, and more. . .

## Slide 5
Interference Emanates in Many Forms
RF Record & Playback Need for Interference Identification
Identifying RF Fingerprint
Cannot Always Model or Capture Anomalies in the Lab
Not sure of signals to look for:
  “Desired” signals well understood (Normalizing – Baselining)
  “Problem” signals exist in many forms (Shouldn’t be there)
Need to discover RF signal anomalies
  Characterize precise behavior in multiple domains
  Terabyte memories provide capture times from minutes to days
Critical to create signal archives
  Compare to previous events
  Manipulate and re-transmit signals

## Slide 6
Interference
\ˌin-tə(r)-ˈfir\ : to hinder or impede; come into collision or be in opposition
Photo: Courtesy of CBS Sports

## Slide 7
  Interoperability
  Design Compliance – vendor adherence to a published standards
  Margin Testing - Receiver performance in presence of interference
Compatibility
  Operational Compliance – Transceiver performance in the presence of other mission critical RF assets
  Impacts from and on other RF assets
Goals of Interference Testing

## Slide 8
Culprits
Co-Channel
Adjacent Channel
PIM and Rx De-sense
Harmonics/Spurs
Deliberate Jamming
Jammer
In-Band
Out-of-Band
In
Channel
Out of
Channel
Co-Channel
Adjacent Channel
Noise Floor
Fundamental
Harmonic
High Power Tx
Intermodulation
Victim
Interference In Many Forms
Culprits
Co-Channel
Adjacent Channel
PIM and Rx De-sense
Harmonics/Spurs
Deliberate Jamming

## Slide 9
Monitoring stops while the receiver is post-processing
Events lasting longer than the available memory are lost
Trigger settings valid only for one set of conditions
Challenges with Traditional Approaches
ADC
DSP
RAM
µP
Display
RF
Input
If the system fails to capture the event, it’s gone forever
Signal Analyzer Block Diagram
(simplified)
Preselect
Down- Convert
Digitize
Store
Process
Continuous Processing
Batch
Processing
Real-Time LVDS Interface

## Slide 10
Alternative Approach
Interference Testing – Workflow
RF Down Conversion
Signal Playback
Waveform Digitization
Signal Capture
Data Formatting & Storage
RF Up Conversion
Waveform Generation
Signal Analysis & Signal Creation
Vector Signal Analyzer w/ Streaming IQ Interface
  Broad frequency coverage
  Wide acquisition bandwidth
  High dynamic range
IQ Data Recorder
  Real Time Data Tagging
  High Speed Offloading
  Data Protection
Visualize & ID Signals
Replay Very Large Files
Create New Signals from
Original Data
Convert Digital IQ to Analog
Vector Signal Generator
  Broad frequency coverage
  Wide bandwidth IQ
  High dynamic range
Analyze and Simulate
100% Capture, Analysis, Simulation and Replay RF Data

## Slide 11: HW Tools for Interference Testing
IQC5000B RF Record & Playback System
  40, 165, & 255 MHz IBW
  16-bit Low Voltage Differential Signaling (LVDS) interface
  Built-in IQ and fixed RF playback
  IRIG-B and GPS Inputs
  Triggers and Markers
  Memory
    Internal: 50 min @ 255 MHz
    External: 3 hours @ 255 MHz
  Single and Dual Channel
  Utilizes RSA for down conversion & digitization
IQC91000A RF Record & Playback System
1000 MHz IQ record and playback bandwidth
1 GHz to 18 GHz frequency coverage, 26.5 GHz and 40 GHz option available.
90 minutes of continuous record and playback time.
High-speed data offload for post-processing in MATLAB® as well as other popular VSA tools.
Sophisticated triggers and markers to time-tag and geo-tag signal events.
Eliminate gaps and only record signals of interest by leveraging gated trigger capability.

## Slide 12
Spectro-X Signal Analysis Software
  Visualize stored data as a “Motion Picture”
  Search engines to ID and fingerprint waveforms
  “Clip and Save” for replay in VSA SW
Vector Signal Analysis Software
  Supports over 75 standards and modulation types
  Bit-level modulation analysis
RF Editor Signal Creation Software
  Create new signal scenarios from recorded files
  Clip, stitch, translate, filter and loop waveform libraries
SW Tools for Interference Testing
VSA Software
Spectro-X Analysis
RF Editor Software

## Slide 13
#1. Record in theater & playback in the lab
  Characterize the nature of interference
    100% capture provides understanding of who, what, when and where
    Record environment at victim and culprit locations simultaneously
    Extract and post-process interesting portions from long-duration captures
  Replay and Simulate environment using real-world signals
    Test receiver in presence of interference
    Evaluate mitigation techniques
Use Cases for Interference Test

## Slide 14
#2. Record in the lab & playback in the lab
Use Cases for Interference Test
  Compatibility testing during long-duration integration test
  Anechoic chamber and direct inject measurements

## Slide 15
#3. Create in the lab & playback on the range
Use Cases for Interference Test
  Interoperability testing
  Single and multi-channel environment simulation
  Communication Regulation Organizations
    Spectrum Management
  Disaster Relief Organizations
    Communication Effectiveness
  Space Exploration Agencies
  Science & Technology Agencies
  CERN Hadron Collider
    Black Matter Research
    Axion Particle Research

## Slide 16
10 Minutes of Continuous Capture
Visually Inspect for Interference
Zoom into Interesting Time Ranges
Signal Process
Case Study – Bluetooth, Linear FM Chirps
Region #1
Region #2
Region #3
Spectro-X

## Slide 17
Case Study – Region 1
Select Time of Interest
Question: How often do signals like this one occur?
Spectrogram
Zoomed
Spectrogram
Zoom on Signal of Interest
IEEE 802.11b
Analyze Signal of Interest
88 µs
Time Overview

## Slide 18
Carrier Search
  Finds all signals above a specified power threshold
  Prune results to isolate signals of interest
Case Study – Region 1 Interference
Find Everything
Sort on Signal Characteristics

## Slide 19
Carrier Search
  137,000 total carriers found over time range
Search Pruning
  5,000 matching our criteria for hopping radio
  Center Frequency
  Bandwidth
  Start Time
  Duration
  Power
Spectrogram for each result
Hop Freq vs. Time
10.2 Seconds
Case Study – Region 1 Interference

## Slide 20
Region #2
Culprit Easy to See
Questions:
What is the interfering signal?
What is the impact on the 801.11g signal
quality?
Time Overview
Case Study – Region 2 Interference

## Slide 21
Waveform Search
  Correlate training sequence in wireless standards
  User-definable carrier frequency and correlation
  Stepping allows searching “near” specified carrier frequency
Case Study – Region 2 Interference

## Slide 22
Time before Interference
Time during Interference
Extract Portions of Dataset for Time-Correlated Vector Signal Analysis with VSA Software
Spectro-X Spectogram
45 dB
Case Study – Region 2 Interference

## Slide 23
Case Study – Region 3 Interference
Questions:
How many instances occurred?
Which ones are not like the others?
Zoom on Signal of Interest
Spectrogram
Signal appears to be a 10 MHz LFM Chirp
Zoomed Spectrogram
Region #3
Time Overview

## Slide 24
Waveform Search
  Find occurrences of signals that look like a reference waveform
  Reference can be extraction from data set or simulated (e.g. MATLAB)
  User-definable correlation and carrier frequency
Reference Waveform
Case Study – Region 3 Interference

## Slide 25
Waveform Search
  20,000 occurrences matching the reference
Case Study – Region 3 Interference
“Good” Pulse 99% Correlation
“Bad” Pulse 21% Correlation

## Slide 26
Case Study – Region 3 Interference
Spectrum
Phase v Time
Freq v Time
Amplitude v Time
Export pulse to VSA SW to show why it's different

## Slide 27
Region #1
  Found 137,000 total carriers
    Pruning extracted frequency agile radio with 5,000 hops
    Hopper operated for 10.2 seconds starting 11:31am
    Hop pattern was extracted and plotted using Excel
Case Studies – Interference Results
Region #1
Region #2
Region #3
Analyze Signal of Interest

## Slide 28
Region #2
  Identified an 802.11g transmission
    Interferer began disrupting communications at 11:34 am for 5 seconds
    VSA analysis found that EVM went from 2.6% when interference was not present to nearly infinite when the interferer was present
Case Studies – Interference Results
Region #1
Region #2
Region #3

## Slide 29
Region #3
  Located 20,000 occurrences of an arbitrary carrier that looked like an LFM radar chirp
    Correlation analysis found that one pulse looked different (21% match) at 11:38:46.692am
    VSA analysis found that this was a 10.7us wide non-linear chirp
Case Studies – Interference Results
Region #1
Region #2
Region #3
“Good” Pulse 99% Correlation
“Bad” Pulse 21% Correlation

## Slide 30
Filtering – Improve receiver preselection
Shielding – Reduce impact of culprit radiation
Spatial Separation – Take advantage of path loss
Re-banding – Find compatible open channels
Temporal Compliance – Timing of culprit and victim
PIM Studies – ID interference and use hand-held tools to locate
Margin Testing – How much is enough to mitigate interference effects
Mitigation Strategies

## Slide 31
Choose Recordings
From Library
Loop segments at specific intervals
Add frequency shifted copies of original signal
Filter signals to reduce transition transients
Create composite IQ file
Independent, parallel tracks can be precisely time synchronized
Build New Scenarios from Existing Recordings
Tools – Signal Editing and Creation

## Slide 32
Extract time segment of “good” WLAN operation (no interference)
Overlay the interference waveform
Build new signal environment to simulate and test
  Attenuate culprit
  Sum with “good” WLAN signal
  Simulate scenario and replay into victim receiver
+
=
48 dB Attenuated Culprit
Good WLAN
Composite Signal
Original Level
Test Level
Mitigation Example for 802.11g Interference

## Slide 33
EVM still impacted, but worse-case acceptable
Mitigation Example for 802.11g Interference

## Slide 34
Create RF Environments using Recorded Waveforms
  IQC5000B – formats the data for replay at baseband
  IQC5000B – converts signal from digital IQ to analog IQ
  VSG – up converts the IQ waveform to carrier frequency
Mitigation Example for 802.11g Interference
RF Down Conversion
Signal Playback
Waveform Digitization
Signal Capture
Data Formatting & Storage
RF Up Conversion
Waveform Generation
Signal Analysis & Signal Creation
Analyze and Simulate

## Slide 35: Interference Testing Summary
Interference Comes in Many Forms
  Not always easy to see or determine the culprit
  Alternative approaches may be required
Signal Processing Tools are Often Required
  Understand the nature of the interference
  Understand its impacts on system performance
Captured Interference is Information
  Provide undeniable proof of what actually happened
  Use to stress and margin test victim receivers
Photo: Courtesy of Flickr.com

## Slide 36
SALES
Julian Parker
(571) 612-5490 (office)
(703) 297-6055 (mobile)
julian.parker@xcomsystems.com
APPLICATIONS ENGINEERING
Alex Botten
(571) 612-5486 (office)
(571) 334-3193 (mobile)
alexander.botten@xcomsystems.com
Sales & Applications Contacts
High Speed
RF
Data Capture | Analysis
Detection | Generation
X-COM Systems LLC
A Bird® Company